## Slide 2: Snell Standards and Research for Better Protection
Hong Zhang
IRETS/MSF
August 26-28, 2019
Columbus, OH

## Slide 3: Beginnings
Amateur Racer William “Pete” Snell
Rollover Crash in Arcata, California,
  August 6, 1956
Pete died of head injuries
  Sustained in a then state-of-the-art helmet
Notes: William “Pete” Snell died of head injuries received in an amateur racing crash in 1956. He had been wearing what was then a state of the art helmet but which failed to prevent fatal head injuries in what was otherwise said to be a survivable crash.

## Slide 4: Helmet in 1950s

## Slide 5: How to Choose among Today’s Motorcycle Helmets?

## Slide 6: Snell Motorcycle Helmet Standards

## Slide 7: Effectiveness of Standards
Standards = Documents
Effectiveness of standards depend on
* Strict and independent certification
* Enforceable compliance
* Experience and competence
Testing and More Testing

## Slide 8: Not how Snell tests helmet

## Slide 9: Oldest Snell Testing Photo

## Slide 10: Old Oscilloscope Early 1960s

## Slide 11: Snell Test Lab Today

## Slide 12: Snell Impact Test

## Slide 13: Snell Penetration Test

## Slide 14: Roll-off Test

## Slide 15: Snell Face Shield Test

## Slide 16: Some fail tests.

## Slide 17: Some pass tests.

## Slide 18: Scientifically Valid & Repeatable Test

## Slide 19: Experience and Expertise

## Slide 20: Snell Certification Program
Tough Standard Requirements
  To ensure best protection available
Certification
  To determine Worthy Helmets
Random Sample Testing
  To assure compliance of helmets in markets

## Slide 21: Snell Certification/RST Testing

## Slide 22: Snell – Most Stringent Standard

## Slide 23: Snell Updates Standards Every 5 Years M2020 Standard Effective Oct. 1, 2019

## Slide 24: Newer Helmets and Greater Protection
The effectiveness of helmet has increased from 29% between 1982-1987 to 37% between 1993-2002.(NHTSA reports)
Tougher Snell Standards
DOT Standard Unchanged
Better Designs and Materials

## Slide 25: Shell Spreads the Load. Liner Foam = More Braking Time
Notes: This is an example of what impact can do. This is a tested helmet which was sawn in half. You can see what test impacts have done in the front. The shell has recovered but the stiff liner has been permanently crushed. It has actually recovered some of it’s thickness. During the impacts, it was squeezed much thinner. Snell helmets need every bit of their wall thickness to pass the tests. Of course, a smaller hit wouldn’t require as thick a liner but if that thinner walled helmet was to get a major hit, once the liner was used up the rest of the damage would go to destroying our test head form; or some rider’s head.

## Slide 26: Research Snell vs DOT

## Slide 27: Snell Protects/DOT Bottoms Out

## Slide 28: Fact Check
Misinformation that Snell helmets are only for racers.
DOT is NOT all you need.
Snell helmets are NOT too hard.
    Snell & DOT protect the same in minor impacts.
    Snell continues to protect at higher levels long after DOT protection fails.

## Slide 29: International Conference of Biomechanics Research (IRCOBI)
September 2015 in Lyon, France
Snell Presents Peer Reviewed Research Paper
Low Energy Impact Comparison Study
Snell and NOCSAE Sponsor a Seminar on Test Method for Angular Acceleration

## Slide 30: Three Helmet Standards (US)
ECE and DOT (FMVSS 218)
  Mandatory – minimum impact protection requirement
  DOT Self-certified /ECE Not as protective
    Manufacturers arrange “reasonable” testing
    Claim DOT certification for their own products
Snell M2015
  Voluntary – premium impact protection capability
  Snell certified
    Snell does pre-market and in-market testing
    Manufacturers are bound by contract

## Slide 32: Snell Means Premium Protection. DOT and ECE are Minimum Requirement.

## Slide 33: Motorcycle Helmet Effectiveness
NHTSA estimates that helmet usage leads to:
37% reduction of crash fatality
67% prevention of brain injuries

## Slide 34: Other Snell Standards

## Slide 35: NASCAR & INDY 500

## Slide 36: Austin Dillon Walking Away from 2015 Crash NASCAR Daytona Finish

## Slide 37: Helmet Fit Research
Well-fitted helmets protect better.
Dr. Amy McIntosh reported in 2012 that children with help fitting a helmet had concussions reduced by 41%.

## Slide 38: How Helmets Work
Space
Time
Cartoon Videos on YouTube.com

## Slide 39: Wireless Head Form for Rotational Impact Test

## Slide 40: Bridging Vein Rupture

## Slide 41: Shell Spreads the Load. Liner Foam = More Braking Time
Notes: This is an example of what impact can do. This is a tested helmet which was sawn in half. You can see what test impacts have done in the front. The shell has recovered but the stiff liner has been permanently crushed. It has actually recovered some of it’s thickness. During the impacts, it was squeezed much thinner. Snell helmets need every bit of their wall thickness to pass the tests. Of course, a smaller hit wouldn’t require as thick a liner but if that thinner walled helmet was to get a major hit, once the liner was used up the rest of the damage would go to destroying our test head form; or some rider’s head.

## Slide 42: Physics in a Thumb Tack

## Slide 43: Hard Shell /Spread the Force

## Slide 44: Skull Fracture and Hemorrhage

## Slide 45: Snell Helmets Save Lives.

## Slide 46: Snell Tests For Public Safety
  Snell Web Site Helmet List
  Updates Each Day
  Certified Helmets by Name and Size
  Decertified Helmets Noted

## Slide 47: Snell’s Mission
Evidence based Helmet Standards
Premium Protective Helmets
Injury Prevention Education

## Slide 48: SCCA National Hall of Fame 2015

## Slide 49: Helmet Dos and Don’ts
Replace every 5 years.
Fasten chin strap.
Clean with only soap and water.
Do not cut or alter the helmet liner.
Do not put helmet near hot muffler or engine.
Do not place helmet atop mirror or handle bar.

## Slide 50: Snell’s Mission
Evidence Based Helmet Standards
Premium Protective Helmets
Injury Prevention Education

## Slide 51: We Don’t Make Helmet. We Make helmets Safer.

## Slide 52: More Information
Videos in Snell Youtube Channel
  How Helmet Works to Protect the Brain
  Why Helmet Standards Matter
  Snell Lab Tour
  Snell Facebook/Twitter
  Call Snell Lab and Office: 916-331-5073

## Slide 53: Last Words
Riders have no direct indicators of helmet protective capability
Riders can look for indirect indicators
(e.g.:a serialized Snell sticker)
There are reasonably foreseeable crashes that will exceed a helmet’s protective capabilities.
In serious crashes riders need all the impact management capability a helmet can offer.
www.smf.org 916-331-5073 for more info